## Slide 1: Media Capture Description
Mark Duckworth

## Slide 2: Media Capture & Attributes
Capture Sets
Media Capture
Audio or Video
Attributes
Encoding
Group
Media Capture
Audio or Video
Media Capture
Audio or Video
Simultaneous Transmission Set
Notes: This shows the high level organization of information about Media Captures.
This section is mostly about Media Captures and Attributes.
Media Capture is a source of media, from a camera or microphone or other media streams. VC – video capture, AC – audio capture
Media Captures can come from specific devices like microphones and cameras.
Or they can be constructed from multiple devices (mixing, composing, switching).
Or they can be constructed from other media streams by an MCU.
Media Captures have attributes
Media Captures are listed in Simultaneous Transmission Sets – restricts which ones can be used at the same time – more in next sections
Media Captures are associated with an Encoding Group – for alternative encoding parameters – more in next sections

## Slide 3: Attributes
EXTENSIBILITY
Audio attributes
Purpose (role)
  Main
  Presentation
Mixed – true/false
Channel Format
  Linear array
  Stereo
  Mono
Linear position
  0 to 100
Video attributes
Purpose (role)
  Main
  Presentation
Composed – true/false
Auto switched
  True/false
Spatial scale
  Image width
Notes: These initial attributes are used to cover the initial use cases, others can be defined later.
Major tool for extensibility in the framework.
Purpose – main people media, or presentation media.
Mixed – audio is a mix from different sources, such as an MCU mixing most recent speakers.
Channel format – the meaning of the different audio channels.
Linear position – for audio channel format = linear array, this denotes the position from left to right.
Composed – image is composed of multiple input images, for example with PiP or “Hollywood squares” grid layout.
Auto switched – image is switched between multiple sources, for example switched to the current speaker.
Spatial scale – a measure of image width, probably something like the measure of the real size image width in centimeters.
Extensibility Attributes are extensible – new ones can be defined, to support new use cases

## Slide 4: Capture Scene
VC0
VC2
VC1
VC3
VC4
Cameras
People
VC1
VC2
VC0
Capture Scene
Three cameras
Two cameras, moved & zoomed out
Switched (based on voice) with composed PiP
VC5
Notes: Different ways to capture same scene (audio similar)
Different alternatives for same Capture Scene.
Left side of diagram is a top view of 6 people at a table, captured by 3 cameras.
Right side of diagram shows three different ways that scene can be captured and displayed, each using a different number of Video Captures.
The point is for the Media Provider to offer alternatives for Media Consumers that can receive different number of streams.
Could also have alternatives for audio – mono, stereo.
There could be multiple capture scenes - For example another scene for a presentation.

## Slide 5: Capture Set
Each alternative representation of a Capture Scene is a row in a Capture Set
Three cameras
Two cameras, moved and zoomed out
Switched (based on voice), composed PiP
(VC0, VC1, VC2)
(VC3, VC4)
(VC5)
(AC0)
Capture Set Rows
VC0
VC2
VC1
VC3
VC4
VC5
Notes: - Capture Set includes Media Captures from the same Capture Scene
- Capture Set has multiple rows for alternatives and for different media types
- Left to right adjacency of VCs is defined by the order of VCs within a row
There can be multiple capture sets, such as one for people and one for a presentation
This is illustrated for video, but the same concept applies to audio
- audio from the same capture scene is included as additional rows in the Capture Set